## Slide 1: Model-Driven Safety Assessment for robotic systems
Aldebaran Robotics Copyrignt ©

## Slide 2
Romeo2 research platform is now being used to validate the possible service uses for a larger robot than Nao and to test new technologies for possible integration in future Aldebaran products.
The innovations tested on Romeo include human-robot interaction, moving eyes and the vestibular system, force control, etc.
Romeo2 Project
Romeo is a humanoid robot from Aldebaran Robotics which is intended to be a personal assistant and companion

## Slide 3
No standard modeling tools
Modeling language RobotML is based on the UML/SysML standards
Code generation for simulators, middleware/OS and deployment to real robots
Model-driven engineering
of robotic systems
Contexte
Classical safety analysis methods
  Robotic safety standards(ISO13482, ISO10218 ) list risks specific to robotic applications and recommend FMEA and FTA methods for safety analysis
  FMEA and FTA are often performed manually => time consuming, costly, high probability of errors
Design Engineer
Need for safety analysis assistance
Safety Engineer

## Slide 4
Model-Driven Safety analysis
Uniform environment for modeling and safety analysis of robotic applications
Copyright CEA ©
  UML profile for safety analysis
  Own dedicated models
  Strong links between system engineering and safety analysis
Safety Analysis Environment
Notes: MBSE is a convenient way to develop safety-critical systems. This approach relies upon system level models that enable to simulate the overall performance and behavior of complex systems as well as to integrate SA techniques into the engineering process. MBSE environments offer convenient frameworks to integrate different dedicated analysis views within a global design environment.
We propose a modeling framework, called Sophia, for model-based safety analysis. Sophia uses the Papyrus editing tool to leverage features of SysML modeling language and includes facilities to perform different types of safety analysis.

## Slide 5
Safety Life-Cycle
Copyright CEA ©
Functional Hazard Analysis
Concept & Requirements
Design & Optimization
Preliminary System Safety Assessment
Acceptance & Maintenance
Integration & Test
Implementation
System Safety Assessment
Safety Assessment with Sophia
System Development
Validation
Validation
SOPHIA-FTA
SOPHIA-FMEA
SOPHIA-ModelChecking
SOPHIA-PHA
SOPHIA-SHA
SOPHIA-Requirements
Sophia targets early phases of system life-cycle
IEC 61508 generic standard on functional safety
ISO/DIS 13482 safety standard for personal care robots

## Slide 6
Sophia Methodology*
* N. Yakymets, S. Dhouib, H. Jaber, A. Lanusse, “Model-Driven Safety Assessment of Robotic Systems,” 2013 IEEE/RSJ International Conference on Intelligent Robots and Systems, IROS’2013, November 3-7, Tokyo, Japan, 2013.
Copyright CEA ©

## Slide 7
Results
  RobotML model of HW &SW architecture of the Romeo2 robot
  Development a methodology specifying the process of safety analysis of robotic applications related to ISO13482
  Safety analysis of Romeo2 using FME(C)A and FTA techniques recommended by ISO13482
  Automatic report generation
Romeo2: obtained results
Copyright CEA ©
Objectives
  Modeling of Romeo2 software and hardware architecture with RobotML
  Safety analysis of Romeo2 based on RobotML model
Romeo2 Architecture
FMEA Tables
Fault Trees

## Slide 8: Direction DRT Département DILS Laboratoire LISE
Commissariat à l’énergie atomique et aux énergies alternatives
Institut Carnot CEA LIST
Centre de Saclay | 91191 Gif-sur-Yvette Cedex
T. +33 (0)1 69 08 32 93
  Etablissement public à caractère industriel et commercial | RCS Paris B 775 685 019
Thank you!

## Slide 9
Conclusion
Copyright CEA ©
RobotML
  Extends UML for robotic domain
  Extra feature of papyrus http://www.eclipse.org/papyrus/
  RobotML SDK is available with open-source license
  Standardization: Plan to standardize the RobotML language Ongoing work to standardize the PROTEUS ontology within IEEE ORA working group
  ROMEO2: French national project started in December 2012, Safety analysis for humanoid robots
Sophia
  Integration of safety techniques within a model-driven engineering process
  Support of generic standard on functional safety design IEC61508 and ISO 13482 safety standard (non-industrial personal care robots)
  Modelling of architecture, behaviour and failure logic (SysML and RobotML)
  Automatic document generation
Perspectives
  Take into account propagation of failure behavior while allocating SW to HW
  Tackle a complexity of robotic systems by architecture partitioning and controlling the depth of safety analysis